Giswater table data model
Access Manager
Tables to manage the access to network exploitations for users or roles
Specific feature data
Tables used to
store specific fields for different features
Documents
Document table used by the document management module
Kernel
Tables acting as core tables. These are topology tables (node/arc/connec/element) with catalogs, sector and dma tables.
O&M
Operation & management tables used to integrate information from other collecting data systems
Other
Tables
Interoperability
Integration data from SCADA, CRM, GMAO, WATERLOSS or any database the system needs.
Hydraulic model
Tables to store all data hydraulic model needs. Input data and result data to enable the full comunication with the EPA software

---
Giswater WS table data model
Nomenclator issues
anl_	Result tables of analysis processes
audit_	Result tables of audit processes
cat_	Catalog tables
config_	Configure environment
doc_	Tables used by the document	management tool
element_	Table used by the element	management tool
ext_	External information tables (ERP,	SCADA, background, etc.)
inp_	Tables used to store all the input	information used on EPA software
man_	Tables used to store information about	specific fields for features
om_	Tables used for the O&M module (visits	and mincut)
plan_	Tables used by the master planification	module
rpt_	Tables to store the results of the	hydraulic modelling from EPA software
sys_	System tables to store important data	about different processes and definitions
Tank
man_tank
<<
Manager catalog
cat_manager
DQA
dqa
Soil Catalog
cat_soil
Builder Catalog
cat_builder
Work Catalog
cat_work
Owner Catalog
cat_owner
Exploitation
exploitation
DMA
dma
Presszone
presszone
User for exploitation
config_user_x_exploitation
Manhole
man_manhole
User for sector
config_user_x_sector
Source
man_source
Sector
sector
inventory
Roles
Users Catalog
cat_users
Waterwell
man_waterwell
hydraulics
Polygon
Junction
man_junction
Node
node
Reduction
man_reduction
Node Features
cat_feature_node
Node material Catalog
cat_mat_node
Node Catalog
cat_node
Node documents
doc_x_node
Doc type
doc_type
Valve
man_valve
Exploitation selector
selector_expoitation
Arc documents
doc_x_arc
Hydrant
man_hydrant
doc
Sector selector
selector_sector
Pump
man_pump
Connec documents
doc_x_connec
State selector
selector_state
Filter
man_filter
Meter
man_meter
Events
om_visit_event
Arc
arc
Arc Features
cat_feature_arc
Arc material Catalog
cat_mat_arc
Arc Catalog
cat_arc
Register
man_register
Node visits
om_visit_x_node
Domain value tables
Audit tables
Expansion tank
man_expansiontank
Visit
om_visit
link
Arc visits
om_visit_x_arc
Streeter
Analysis tables
Flexunion
man_flexunion
Connec
connec
Connec Features
cat_feature_connec
Connec Type
connec_type
Connec Catalog
cat_connec
Event parameter
om_visit_parameter
Net Sampleoint
man_netsamplepoint
Connec visits
om_visit_x_connec
Config tables
Master plan tables
Net element
man_netelement
Event type
om_visit_parameter_type
System tables
Mincut tables
Net wjoin
man_netwjoin
Element
element
Element Features
Element_type
Element material Catalog
cat_mat_element
Element Catalog
cat_element
Review tables
Raster tables
varc
man_varc
GMAO DATA
Pipe
man_pipe
Dma
Greentap
man_greentap
Juction
inp_junction
Pipe
inp_pipe
Virtualvalve
inp_virtualvalve
Virtualpump
inp_virtualpump
Shortpipe
inp_shortpipe
Inlet
inp_inlet
Tank
inp_tank
Reservoir
inp_reservoir
inp_valve
Pump
inp_pump
Fountain
man_fountain
WATERLOSS DATA
inp_connec
Tap
man_tap
Hydrometer - connec
rtc_hydrometer_x_connec
Period catalog
ext_cat_period
Node results
rpt_node
Arc results
rpt_arc
Results catalog
rpt_cat_results
Wjoin
man_wjoin
Hydrometer Catalog
ext_cat_hydrometer
Netscenario DMA
plan_netscenario_dma
Result selector
selector_rpt_main
Patterns
inp_pattern
Hydrometer data
ext_rtc_hydrometer_x_data
Netscenario
plan_netscenario
Dscenario demand
inp_dscenario_demand
Dscenario connec
Dscenario controls
Dscenario inlet
Dscenario junction
Dscenario pipe
Dsenario pump
Dscenario pump additional
Dscenario reservoir
Dscenario rules
Dscenario shortpipe
Dscenario tank
Dscenario valve
Dscenario virtualpump
Dscenario virtualvalve
Netscenario Presszone
plan_netscenario_presszone
Hydrometer
ext_rtc_hydrometer
Rules
inp_rules
CRM DATA
Dscenario selector
selector_inp_dscenario
Netscenario Arc
plan_netscenario_arc
Netscenario selector
selector_netscenario
Controls
inp_controls
Scada data
ext_rtc_scada_x_data
Netscenario Node
plan_netscenario_node
Energy parameters
inp_energy
Times
inp_times
Scada features
ext_rtc_scada
Netscenario Valve
plan_netscenario_valve
Curves
inp_curve
Project
inp_project_id
SCADA DATA
Netscenario Connec
plan_netscenario_connec

---
Giswater 3 WS table data model
config	Tables to store sytem/user variables
db_cat	Dictionary of tables, views, rows...
event	Tables used to integrate O&M, using a	strategy of dinamic datamodel
ext_	External information tables (ERP,	SCADA, carto information....
Inp_	Tables used to store all the	information used on EPA software
man	Tables used to store information about	features not stored on node/arc tables
plan	Tables used by the master plan	module
price	Tables to integrate db prices from	other software
rpt_	Tables to store the results of the hydraulic modelling from EPA software
value_	Domain value tables (acting as a	catalog tables)
Tank
man_tank
Users
adm_user
Source
man_source
dma (management)
sector (hydraulics)
Waterwell
man_waterwell
Reduction
man_reduction
Node Type
node_type
Hydrant
man_hydrant
Pump
man_pump
Filter
man_filter
Meter
man_meter
Register
man_register
Arc Type
arc_type
Expansion tank
man_expansiontank
Flexunion
man_flexunion
Net Sampleoint
man_netsamplepoint
Connec Type
Connec Type
Net element
man_netelement
Net wjoin
man_netwjoin
vnode
varc
Pipe
man_pipe
Element Type
Element_type
Management tables
Greentap
man_greentap
Fountain
man_fountain
Pipe
inp_pipe
tank
inp_tank
reservoir
inp_reservoir
valve
inp_valve
pump
Tap
man_tap
Wjoin
man_wjoin
Config
Database catalog
Result topology adaptors
rpt_arcnodearc & rpt_nodearcnode
System
Explitation
inp_selector_sector
inp_selector_state
rpt_selector_result
RTC DMA Parameters
ext_rtc_scada_dma_period
RTC demand
rtc_inp_demand
Rules
Custom demand
inp_demand
Sources
inp_sources
Quality
inp_quality
Mixing
inp_mixing
Reactions
inp_reactions_el (gl)
Hydrometer aggregated data
ext_rtc_hydrometer_data
Hydrometer lastest value
ext_rtc_hydrometer_value
rtc_cat_period
Scada aggregated data
ext_rtc_scada_data
Scada lastest value
ext_rtc_scada_value
Times
Report
inp_report
Options
inp_options
Project
inp_project_id
Hydrometer- connec
Curves
inp_curve (id)
inp_energy_el (gl)
Patterns
Emitter
inp_emitter
Scada Node
rtc_scada_node
Scada Catalog
cat_scada
cat_hydrometer
EPA arc type
inp_type_arc
EPA node type
inp_type_node
SCADA data
(table or view from SCADA)
(table or view from CRM)

---
Giswater 3 UD table data model
config	Tables to store sytem/user variables
db_cat	Dictionary of tables, views, rows...
event	Tables used to integrate O&M, using a	strategy of dinamic datamodel
ext_	External information tables (ERP,	SCADA, carto information....
Inp_	Tables used to store all the	information used on EPA software
man	Tables used to store information about	features not stored on node/arc tables
plan	Tables used by the master plan	module
price	Tables to integrate db prices from	other software
rpt_	Tables to store the results of the hydraulic modelling from EPA software
value_	Domain value tables (acting as a	catalog tables)
Wjump
man_wjump
dma (management)
sector (hydraulics)
Node Type
Outfall
man_outfall
Netinit
man_netinit
Wwtp
man_wwtp
Gully documents
polygon
Storage
man_storage
Netgully
man_netgully
Arc Type
Chamber
man_chamber
Varc
Grate catalog
cat_grate
Conduit
man_conduit
Gully
gully
Siphon
man_siphon
Waccel
man_waccel
Connec type
Element Type
element_type
Raingage
raingage
Database catalog
Conduit
inp_conduit
divider
inp_divider
outfall
inp_outfall
storage
inp_storage
weir
inp_weir / inp_orifice
pump
Orifice
inp_orifice
Virtual
inp_outlet
System
Explitation
RTC DMA Parameters
ext_rtc_scada_dma_period
inp_selector_sector
inp_selector_state
rpt_selector_result
DWF
rtc_inp_dwf
Loading
Temperature
inp_temperature
Buildup
inp_demand
Lid control
inp_lidcontrol (lidusage)
Options
inp_options
Hydrometer aggregated data
ext_rtc_hydrometer_data
Hydrometer lastest value
ext_rtc_hydrometer_value
Scada aggregated data
ext_rtc_scada_data
Scada lastest value
ext_rtc_scada_value
Washoff
inp_sources
DWF
inp_dwf
Inflows
inp_inflows
Pollutants
inp_reactions_el (gl)
Aquifers
inp_aquifer
rtc_cat_period
Hydrometer- connec
Landuses
Groundwater
inp_groundwater
Treatment
inp_report
RDII
inp_rdii
Pattern
Timeseries
inp_timeseries (id)
Scada Node
rtc_scada_node
Scada Catalog
cat_scada
cat_hydrometer
Evaporation
inp_evaporation
Curve
inp_curve (id)
inp_energy_el (gl)
Transects
inp_transects
Coverages
Snowmelt
inp_snowmelt
SCADA data
(table or view from SCADA)
EPA arc type
inp_type_arc
EPA node type
inp_type_node
(table or view from CRM)
Gully visits
om_visit_x_gully

---
Giswater 3 WS/UD view data model
Map tools
Some topology reviewers
Topology builders
Topology repairs
Network editors
Current user state filters
v_state_node (state & psector)
v_state_arc (state & psector)
v_state_connec (state)
Auto Mincut (Class 1)
Rehabit cost
Reconstruct cost
Mincut custom (Class 1)
mincut_valve
_unaccess
Map tools
Some topology reviewers
v_om_psector_x_other
om_other_x_psector
Current user edit inventori filters
selector_expl (exploitation)
Current user edit inp filters
selector_sector (sector)
plan_other_x_psector
v_plan_psector_x_other
Hydraulic analysis export inp file
v_edit_man_tank_pol
v_plan_result_node
v_edit_man_tank
v_plan_node
Hydraulic analysis
Import rpt file
Current user export inp filters
inp_selector_rpt (result_id)
v_edit_node
om_rec_result_node
v_edit_man_manhole
inp node tables
inp_
v_om_psector_x_node
om_node_x_psector
v_edit_man_source
Inp node views
v_inp_
om_reh_result_node
v_edit_man_waterwell
v_plan_psector_x_node
v_edit_man_junction
cat_parameters
Current user epa result filters
inp_selector_result (result_id)
inp_selector_result_compare
PRICES
price_simple
price_compost
plan_node_x_psector
v_edit_man_reduction
v_plan_psector
Work X Prices
v_edit_man_valve
Parameters X works
plan_arc_x_psector
v_om_psector
cat_works
v_edit_man_hydrant
v_plan_psector_x_arc
rpt_inp_node
v_edit_man_pump
om_reh_result_arc
v_rpt_node_result
v_edit_man_filter
om_arc_x_psector
v_node
v_om_psector_x_arc
v_edit_inp_reservoir
v_rpt_node_compare
v_edit_man_meter
v_state_node
v_edit_inp_tank
om_rec_result_arc
v_edit_man_register
v_edit_inp_junction
v_edit_man_expatank
v_edit_inp_valve
v_plan_arc
v_plan_result_arc
v_edit_man_flexunion
v_edit_inp_pump
pavement_x_arc
v_edit_man_netsample
v_edit_man_netelement
cat_pavement
System automatic user filters
om_psector_selector
v_edit_man_netwjoin
v_arc
v_rpt_arc_result
v_edit_arc
v_state_arc
v_edit_inp_pipe
v_rpt_arc_comapre
v_edit_man_varc
Current user plan filters
selector_psector
rpt_inp_arc
v_edit_man_pipe
v_edit_connec
v_state_connec
v_edit_man_greentap
anl_mincut_
result_valve
v_anl_mincut_result_valve
v_edit_man_fountain
anl_mincut_
_selector_valve
inp arc tables
inp_
v_edit_man_tap
anl_mincut_
result_polygon
v_anl_mincut_result_polygon
v_edit_man_wjoin
Inp arc views
v_inp_
v_edit_vnode
anl_mincut_
result_node
v_anl_mincut_result_node
v_edit_link
anl_mincut_
result_arc
v_anl_mincut_result_arc
anl_mincut_
result_connec
v_edit_element
v_anl_mincut_result_connec
anl_mincut_result_
hydrometer
Mincut (class 2 o 3)
Connec/hydrometer
v_anl_mincut_result_hydro
Sample
Point
v_edit_samplepoint
v_edit_dimension
Dimension
Current user mincut result filters
anl_mincut_result_selector (result)
Current user edit inventori filters
selector_state (state)

---
Giswater 3 WS/UD config data model
Audit cat functions
sys_feature_type
Inp node type
inp_node_type
Config param system
Catalog of mat node
Audit cat error
sys_feature_type
Config param user
Node type
Feature type
sys_feature_type
System feature catalog
sys_feature_cat
User feature catalog
cat_feature
Config client forms
Macro dma
cat_feature
Connec type
Exploitation
cat_feature
dma
cat_feature
Config web fields
Arc type
Sector
cat_feature
Config web forms
Catalog of mat arc
Inp arc type
inp_arc_type
value_state type
Value state
sys_feature_cat
Psector (alternative)
Mincut state
anl_mincut_cat_state
Street axis
man_addfields_parameter
man_type_category
Users catalog
cat_users
Address point
cat_feature
man_type_fluid
man_addfields_value
Prices
Mincut catalog type
anl_mincut_cat_type
man_type_function
Mincut catalog class
anl_mincut_cat_class
man_type_location
Dscenario catalog
Mincut catalog cause
anl_mincut_cat_cause
value_verified
Pressure zone